## Slide 1
Ethernet Header
IP Header
TCP Header
Data
FCS
Network Interface Layer | Internet Layer | Transport Layer | Application Layer | Network Interface Layer
Direction of data being received (Process)
Direction of data being sent (Transmit)

## Slide 2
Ethernet II |  |  |  |  |  |  |  | 
Preamble |  | Destination MAC Address | Source MAC Address | Type | Data |  |  | FCS
8 byte |  | 6 byte | 6 byte | 2 byte | 46-1500 byte |  |  | 4 byte
IEEE802.3 |  |  |  |  |  |  |  | 
Preamble | SFD | Destination MAC Address | Source MAC Address | Frame Length | LLC | SNAP | Data | FCS
7 byte | 1 byte | 6 byte | 6 byte | 2 byte | 3 byte | 5 byte | 46-1492 byte | 4 byte

## Slide 3
0 |  | 3 | 4 |  | 7 | 8 |  | 15 | 16 |  | 18 | 19 |  |  | 31 | bit | 
Version |  |  | Header Length |  |  | Type of Service |  |  | Total Length |  |  |  |  |  |  |  | IPv4 Header
Identifier |  |  |  |  |  |  |  |  | Flags |  |  | Fragment Offset |  |  |  |  | 
TTL |  |  |  |  |  | Protocol |  |  | Header Checksum |  |  |  |  |  |  |  | 
Source IP Address |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Destination IP Address |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Options |  |  |  |  |  |  |  |  |  |  |  |  |  | Padding |  |  | 
Upper Layer’s Header + Data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 4
Start
Check for connected network device(s)
Choose a connected network device
Any connected device(s) found?
Start capture packets
Add packets information from SharpPCap
Cross search GeoLite2 & add geolocation information to packet’s information
Check if source & destination IP address is private/reserved
Check protocol type filter
(TCP-only or UDP-only or TCP & UDP)
List found connected network device(s)
End
Add overlay to map for packet’s movement
Continue capture next packet
Display all packet’s information in order of :
Protocol, Time of Capture, Length, Source IP Address, Source City, Source Port, Destination IP Address, Destination City, Destination Port
Stop capture?
Yes
No
True
No
No
False
Yes
Yes
Packet Capture
Visualisation
Assign geolocation as private/reserved